## Slide 1: A 13th Magnitude Asteroid Occultation Close to the Full Moon
By Paul D. Maley, Carefree, AZ and Tony George, Scottsdale, AZ
International Occultation Timing Association (IOTA)
Presented at the IOTA Annual Conference July, 2016

## Slide 2: INITIAL CONDITIONS
13.2 MAG STAR
12.7 MAG ASTEROID BOLIVIANA
Δm=0.5
Duration = 9.7 seconds
Moon phase 100%
Moon offset 3 deg
Elevation 30 deg directly over Phoenix light bubble
SKY=CLEAR

## Slide 4: WHAT TO DO WITH AN EVENT LIKE THIS?
REJECT IT AS IMPOSSIBLE?
TRY IT OUT OF DESPERATION?
USE IT AS A TEST OF SYSTEM CAPABILITIES?

## Slide 5: C11 AND OBSERVATION SITE

## Slide 6: PREPOINT SET UP 1.5 PRIOR

## Slide 7: MY VIEW OF ZR80 CAMCORDER SCREEN 14 minutes AFTER CLOSEST APPROACH TO THE MOON OF STAR

## Slide 9: DETECTION FOR ANALYSIS
FOR THIS CASE, CLOCK DRIVE WAS ON
LIMOVIE CAN PROCESS WITH DRIVE ON OR OFF
30 SECONDS OF VIDEO IS THE MINIMUM NEEDED TO DETECT BASELINE NOISE
MORE VIDEO IS BETTER

## Slide 10: REGISTAX STACKED IMAGES
DUST MOTES
DEAD PIXELS
STARS

## Slide 11: GUIDE CHARTS: WHAT I FAILED TO SPOT
PREDICTED EVENT TIME

## Slide 12: C2A ACTUAL FIELD OF VIEW OF FINAL IMAGE

## Slide 13: HOW FAR OFF THE PLANNED FIELD: ~90 SECONDS

## Slide 14: PHOTOMETRY
BLANK FIELD:
NO STAR
10.3 MAG STAR
12.3 MAG STAR

## Slide 15: Occular detectability of a 12.2 magnitude star with a Δm=2.0

## Slide 16: Occular detectability of a 10.388 magnitude star with a Δm=0.5

## Slide 17: Minimum Occular dectability of a 10.388 magnitude star with Δm=0.5

## Slide 18: PALLAS OCCULTATION 7/7/16 dM of 0.08

## Slide 19: PALLAS OCCULTATION 7/7/16

## Slide 20: TONY GEORGE PROCESSING IS LIKE THIS:

## Slide 21: CONCLUSIONS
SOME IMPOSSIBLE THINGS ARE POSSIBLE (WITH CURRENT TOOLS)
SOME THINGS ARE NOT
EVEN THOUGH OCCULTATION FAILED, GOOD THINGS WERE LEARNED
WITH EQUIPMENT AND CONDITIONS DEFINED ABOVE:
DETECTING A 13.2 MAG STAR WITHIN 3 DEG OF 100% MOON IS NOT POSSIBLE
DETECTING A 10 MAG STAR WITH Δm=0.5, DURATION>3 SEC IS POSSIBLE
DETECTING A 12.2 MAG STAR WITH Δm=2.5, DURATION>10 SEC IS POSSIBLE