## Slide 1: Three Short Presentations
Joan Dunham
July 26, 2020

## Slide 2: SkyWatcher + QHY Camera
Joan and David Dunham

## Slide 3: Example of Preparation to Observe
16” SkyWatcher GOTO scope
  Collapsable Dobsonian
  Used as a transportable scope, not on a fixed mount
  Used and stored on a Scope Buggy
QHY 174 GPS Camera
  Data capture with SharpCap
RunCam Mighty-Mini Finder
  Display to portable video screen or Win10 tablet with IOTA Video Capture
TalentCell 12V/6000mAh batteries
  2 - one to power the scope, the other for the cameras
Dell Laptop running SharpCap for data collection

## Slide 4: Steps in Preparation to Observe
Collimate the scope
Attach the camera and finder and adjust the finder, if needed, to align with the telescope
Perform star alignment of the telescope
Find the target
Record the event

## Slide 5: Collimate
Collimate first, before powering the telescope
Collimate this scope every time
Collimate carefully, it is possible to pop the primary completely out if the screws are run close to their limits

## Slide 6: Video Finder
RunCam NightEagle 2 “Astro Edition”
Mighty-Mini
  Finder-scope version
  Cylinder built with a 3-D Printer by J. Moore
Alignment to scope
  Check with bright object – Moon or Jupiter
  Mark the center of the scope FOV on the finder video display with painter’s tape
  If scope FOV not on the finder – check the finder for attachment or other problems

## Slide 7: Camera and Finder Attached
Note the number of cables and cords – 2 power cords, video cable, USB cable, GPS antenna cord

## Slide 8: Observing Table
Freestanding
Holds
  Video display + battery
  Finder charts
  Laptop running SharpCap + mouse
  Flashlight
Must be moved with the scope when it slews
  Avoid stress on the camera cables
  Requires 2 people, one to operate the scope, the other to carry the table

## Slide 9: Align the Scope
2-star alignment preferable for asteroidal occultations
Check alignment by commanding scope to another, nearby, target
  Use PAE (position accuracy enhancement) if it is close but not close enough
Things that can go wrong
  Mis-identification of an alignment star; some stars have other bright ones nearby
  Coordinates or date/time entry error on set-up

## Slide 10: Find the Target
Tools to use
  Scope’s catalog if it has the target star
  Finder charts + add the target star position as a user object
  Google Sky to augment the finder charts
Problems
  Target area doesn’t match finder charts
    Camera is red sensitive, red stars are brighter/blue stars fainter than catalog visual mag
    Asteroid in FOV can look like an unexpected star
    More stars in the FOV than on the finder charts – Google Sky will show them
  On target area, don’t see target, and event time is close
    Increase exposure and/or gain
    Take the data anyway – postprocessing may find the target