## Slide 1: Equipment Aids of My Dreams
Joan Dunham

## Slide 2: Desirable Observing Aids
Enhanced prepoint finder charts
  On a laptop or tablet instead of paper
  Night mode lighting
  Screen display progresses with time as the event approaches
  Drill-down through displays to get to finer and finer detail
  Display customizable to match screen display or FOV of scope
Ability to configure Windows computer to be better at data capture
  Provide option for “stripped” mode, removing apps not needed for data capture
  Maximize data capture priority
  Batteries that are easily replaced

## Slide 3: Camera Wishes
Camera with IOTA VTI-like GPS capability
Increased sensitivity
Weather (dew) resistant
Inexpensive
On-board temporary capture to minimize dropped frames
Possible scenario for current camera designs upgrade
  Data time-tagging and temporary storage between camera and capture computer
  Allows high speed data capture which is then forwarded as the capture computer can accept it

## Slide 4: USB Comments
USB standard emphasizes ease of use and low expense , not precision
Issues like these
  Short USB receptacle, long USB plug
  Short USB plug, long USB receptacle
  Loose fitting USB plug, falls out
  Tight fit, plug can damage receptacle
USB 3.0 standard does not specify a maximum cord length but the maximum practical length for copper wiring to meet the electrical specs is 3m (9.8 ft)
USB tester – like the Eversame USB Type C tester - helps in resolving problems
Occasional poor communication when this plug, which is a little too long for the receptacle, is not straight.

## Slide 5: USB Digital Tester
No communication – note the amps are shown as 0.
Communication – the amps are >0.

## Slide 6
USB specifications overview from Wikipedia
USB 2 has 4 pins, all on one side
USB 3.0-3.2 has 9pins, 4 on one side, 5 on the other
USB C has 24 pins, 12 per side
USB C is shown as for USB 3.1 and higher. But some early designs may have only implemented USB-2 options in a USB C plug/receptacle.
The QHY-174 camera USB receptacle is Type B USB 3. This type of connector will not be an option for higher speed USB 3.3 or USB 4.
Note that, in the future, everything but the Type C USB connector is deprecated. In the future we can discard our various cords with different connectors as well as multiple types of adaptors. Also, since the USB C is used for power cords, we no longer will need separate power cords for each device.